H-SHELTER

The H-element was inspired by the ancient chinese self supporting bridge structures and Leonardo da Vinci's concepts on the same subject.

The proposed low-thech constructions are aiming to offer a cosy shelter (day and/or night) for the traveler by using only three materials: wood, iron, awning.

The building is in fact a self supporting wooden structure which allows a great variety of forms and both architectural and aesthetic solutions. Because of its simple construction principle it can be introduced in mass production as well, and can be a low cost solution for real practical use.

The materials to be used and the installation structure are strong enough to withstand against even adverse conditions and intensive usage.

In our estimation the life expectancy for the H-Shelter structures can be at least 5 years and will have zero impact on their environment.

No maintenance needed.

Strategy for on-site prototype:

The prefabrication of the 'H' elements and the building process can be accomplished in around 15 days by two builders.

Material request:

5 x 5 x 400 cm red pine laths

16 mm diameter threaded rods, washers, nuts, screws

Equipment request:

drill-press, electric circular saw, electric screwdriver, electric grinder, rope

Major dimensions:

Day_Shelter: 265 x 375 X 230 cm

Night_Shelter_Family: 370 x 320 X 180 cm

Night_Shelter_Single: 180 x 250 X 150 cm

Support:

Incidentally for loading and transporting the materials to the location.